## Slide 1: Python In ChemE End Term Evaluation
ARMEET LUTHRA

## Slide 2: Assignment 1 : STOKES LAW
Problem statement :
In this assignment we were required to compare the analytical and numerically calculated terminal velocity of a sphere in a medium of given density and viscosity.
Physics and equations :
A freely falling spherical ball experiences three forces:
Gravitational force downwards,
Buoyancy upwards,
Drag force, which acts opposite to the direction of velocity of the particle

## Slide 3: Assignment 1
The equation of motion can be written as: mdu/dt=mg-⍴Vg-6πrηu.
m=mass of sphere
u=velocity of sphere
g=gravitational acceleration
⍴=density of fluid
V=volume of sphere
r=radius of sphere
η=viscosity of the fluid

## Slide 4: Assignment 1
Algorithm
1) Input the necessary parameters (density of liquid, sphere, viscosity of liquid, radius of sphere, tolerance and integration time step)(initial velocity of sphere is assumed to be 0)
2) The equation of motion is integrated using linear approximation to integral:
du/dt≃[u(t+Δt)-u(t)]/Δt
u(t+Δt)=gΔt(1-⍴V/m) +u (t)[ 1+6πrηΔt/m ]
3) This is implemented using a loop incrementing the Δt each time till the error between u(t+Δt) and u(t) is less than the given tolerance.
4) The final u will be the terminal velocity
5) Analytical terminal velocity Is calculated by putting acceleration=0 in the equation of motion.
6) For a sphere it comes out to be: vt=(⍴s-⍴l)*g*r2 *2/(9*n)

## Slide 5
Python Code

## Slide 6: Output

## Slide 7: Assignment 2 : Heat Diffusion Equation
Problem Statement:
In this assignment we were required to find the TEMPERATURE PROFILE OVER TIME for a flat plate, subject to certain fixed boundary conditions and also animate the changes. This was done by solving the Heat diffusion equation.
Physics of problem
The heat conduction equation at steady state is given by:

## Slide 8: Assignment 2

## Slide 9: Python Code

## Slide 10: Output
Initial boundary condition: Top edge at 100o, rest plate at 0o. Final temperature profile for this case is :

## Slide 11: Output
2. Initial boundary condition: Top edge at 100o, Right edge at 50o, rest plate at 0o.Final temperature profile for this case is:

## Slide 12: Animation

## Slide 13: Assignment 4 : Double pipe heat exchanger
Problem statement :
In this assignment we were required to solve and obtain the transient response of Temperature with time for the given concentric cylinder double pipe heat exchanger for co-current flow.

## Slide 14: Assignment 4
Physics and equations :
Using energy balance:
The heat balance equation for concentric heat exchanging cylinders is:

## Slide 15: Assignment 4

## Slide 16: Assignment 4 : Algorithm

## Slide 17: Assignment 4 : Algorithm

## Slide 18: Python Code

## Slide 19: Output

## Slide 20: Output
2) Temperature profile color map at some instant

## Slide 21: Animation